## Slide 1: CS341 Lab 6:
Driveway light
https://github.com/whittyh/CS341

## Slide 2: Lab 6 Objectives:
Create a driveway light that turns on with motion at night
Interface with a Motion Sensor to detect motion
Interface with a PIR to detect light

## Slide 3
Infrared Motion Sensor:
Detects motion by measuring changes in heat
Digital sensor, returns a 1 or 0 depending on motion:
  1 = motion
  0 = no motion

## Slide 4: Photoresistor:
A form of variable resistor that changes resistance based on the light that hits the sensor
Analog sensor, requires analog input and returns a value based on the amount of light detected.
Rather than a 1 or 0 (digital sensors) we get a value of range 0-1023 that represents the light sensed.

## Slide 5: Analog (and Digital) Pins:
Digital Pins
Analog Pins
Analog Pins:
Read voltage between 0-5v
Interprets voltage as value between 0 – 1023
Analog pins can be used for digital sensors but not vice versa
Example of reading from an analog pin:
analogRead(A0);

## Slide 6: Approach:
Complete circuit and implement the following logic:
  Loop() {
  if (motion) {
  if (light < 200) {
  // light bulb on
  delay (waitTime);
  }
  } else {
  //turn the light off if there's no motion
  }
  delay(200);
  }

## Slide 8: Useful Functions:
// is there any motion?
digitalRead(motionPin) // will return HIGH or LOW
digitalWrite(nightLight, HIGH) // turn on the light
// reads the light value (returns 0-1023)
analogRead(lightPin)