## Slide 1: CS341 Lab 9:
Measuring a function
https://github.com/whittyh/CS341

## Slide 2: Lab 9 Objectives:
Use function generator and oscilloscope to learn about function waves
Measure frequency

## Slide 3
Waves:
Pulse Width: how long the signal remains HIGH
Period: The time it takes for the wave to repeat
Frequency: 1/Period
  We can think of frequency as a measure of how dense the wave is

## Slide 4
Function Generator:
Outputs a wave-like electrical signal
Settings:
  Frequency: how many times the wave will be repeated in 1 second
  Amplitude: The difference in voltage between the top of the wave and the bottom of the wave
  DC Offset: the voltage amount that the wave is centered at
  Function: change between rectangular, smooth, or triangular wave

## Slide 5: Oscilloscope:
Visually observe the wave function:

## Slide 6: Part 2:
Create an Arduino program that reads a digital signal and calculates:
  Period:
    Time from peak to peak of wave
  Frequency:
    1 / period
  Pulse width (optional):
    Time wave signal is ‘high’
Some tips:
  Display numbers in seconds
  Serial.println(frequency, 5);
  Be careful of division between two integers

## Slide 7
The Starter Code: