## Slide 1: CS341 Lab 7:
Velocity and Distance
https://github.com/whittyh/CS341

## Slide 2: Lab 7 Objectives:
Use an ultrasonic sensor to calculate the velocity of an object passing in front of the sensor
Interface with ultrasonic sensor

## Slide 3
Ultrasonic Sensor:
Digital sensor that sends and receives high frequency ‘ultrasonic’ sound waves, commonly called Sonar
Send ‘ping’, wait a fixed time interval, read ‘echo’
Two common styles, 3 and 4 pin. We use 3 pins
On 3 pin sensors the ping and echo are written and read through the same pin, while 4 pins have separate ping and echo pins.

## Slide 4
Visualizing Sonar:

## Slide 5: Approach:
Complete circuit and implement the following logic in the loop:
  Loop()
  {
  delay(24); // small delay between loops
  d = ping(pingPin); // read distance
  delay(DELTA_T); // delay 1 second
  // calculate distance again (d2)
  // v = (d2 –d)/(time) (note: time = 1)
  // print distance 1, distance 2, and the velocity
  }

## Slide 6
Observe how the ping function works:
(note you shouldn’t change this code)
// set pingPin to write (OUTPUT)
// set low for 2 microseconds
// set high for 5 microseconds
// set low again
// change pinmode to read (INPUT)
// use pulseIn function to return time // taken to receive ‘echo’
// divide time by 29, then by 2 to return correct distance

## Slide 7: Overview:
Use ping function already written to do the following in the loop:
  Read distance
  Wait 1 second
  Read distance again
  Use V = ∆D/ ∆T