## Slide 1: CS341 Lab 4
Memory Mapped I/O
https://github.com/whittyh/CS341

## Slide 2: Lab 4 Objectives:
Repeat lab 1 without special functions like digitalWrite()
Determine which bits in memory control pin 13:
  Use digitalWrite() to change pin 13’s pin mode
  Use functions from previous labs (provided in starter code) to display memory addresses in relevant range
  Identify what addresses are being changed by the digital write
Use Memory Mapping to directly access and change pins by changing certain bits
Use a bitshift and bitmask to read/write specific bits in memory
Use pointers to access the data in certain registers

## Slide 3
Understanding the pins:
Data Register: where we write to
Data Direction Register:
0 for reading, 1 for writing
Input Pins: where we read from
  digital sensors read high/low, 0 or 1
  Analog sensors signal is interpreted with an analog to digital converter into 10 bits of binary, or a decimal number between 0-1023

## Slide 4: Interfacing with a digital pin two ways:
functions: | Memory Addresses:
pinMode(int pin, OUTPUT); | Set data direction bit to 1
pinMode(int pin, INPUT); | Set data direction bit to 0
digitalWrite(int pin, HIGH); | Set data bit to 1
digitalWrite(int pin, LOW); | Set data bit to 0
digitalRead(int pin); | Check value of input bit

## Slide 5: How to find out which register and bits:
displayRAM((char *) 0x020, (char *) 0x02f, true);
  Same as lab 2, example output:
  020: 00 00 00 00 20 00 00 00 00 01 00 00 00 00 00 00
displayBits(0x020);
  Prints contents of address in binary, example output:
  1001111

## Slide 6: Blinking the LED manually example:
Pretend that the address for writing pin 7 is 0x50 and the correct bit for writing is the 6th bit 0100 00002
Then to flash pin 7 we can bitmask with xor (in loop):
And add a delay(1000);
To set pin 7 high we would use a pointer and set the correct bit to 1 (in setup):