## Slide 1: CS341 Lab 5:
LCD display and piezoelectric speaker
https://github.com/whittyh/CS341

## Slide 2: Lab 5 Objectives:
Connect some interesting hardware to the Arduino to further explore interfacing I/O
Write a circular buffer to implement a ticker screen with a message
Beep the piezoelectric speaker on an interval
Use a potentiometer to control the contrast of the panel by changing resistance of the contrast pin

## Slide 3
Programming the LCD:
<LiquidCrystal.h> library abstracts the work of sending data to the display making it easy to program:
lcd.begin(int columns, int rows);
lcd.setCursor(int colums, int rows);
lcd.print(char[] data);

## Slide 4: Hardware:
Potentiometer:
  Varies resistance
Piezoelectric Speaker:
// 1500 Hz tone:
  tone(buzzer, 1500);
  // turn off buzzer:
  noTone(buzzer);
Resistors:

## Slide 5: Steps:
Complete the circuit:
      test by using the starter code before step 2
Implement a circular buffer:
“Welcome CS341 Students! ” // First display this
“elcome CS341 Students! W”. // Then this…
“lcome CS341 Students! We” // and so on…
Tail
Head